## Slide 1: Medium Frequency Currents Interferential (IFT) Therapy
Dr. Vaibhav Kapare
Dept. Of Cardiovascular & Respiratory Physiotherapy MGM Institute Of Physiotherapy Chh. Sambhajinagar

## Slide 2: Objectives
Explain the physical principles of IFT
Provide rationale for the electro-physical and clinical effects of IFT
Discuss clinical applications of IFT
Describe methods and protocol used in applying IFT
Identify indications and contraindications to be considered prior to use of IFT

## Slide 3: Electrotherapy defined by Frequency

## Slide 4: Key Terms
Interferential Currents
  Endogenous electrical currents created by intersecting two sinusoidal medium frequency circuits of slightly different frequencies
Endogenous
  Originating from within
Modulation
  The variation of a property of a wave or signal such as its amplitude, frequency or phase

## Slide 5: What is Interferential (IFT)Therapy?
Developed by Hans Nemec of Vienna, Austria in early 1950’s
Transcutaneous application of alternating medium-frequency electrical currents, amplitude modulated at low frequency for therapeutic purposes- Martin (1996)
IFT is a form of electrical treatment in which two alternating medium-frequency current are used to produce a low-frequency effect.

## Slide 7: Basic Principles of IFT
IFT utilizes the strong physiological effects of low frequency (<150pps) electrical stimulation of nerves without the associated painful and unpleasant side effects associated with low frequency stimulation
Uses amplitude modulation of medium frequency currents to produce low frequency currents which will be more tolerable for the skin.

## Slide 9: The problem of skin resistance in LF stimulators
Skin impedance diminishes with increase of frequency
Z = 1/2 π FC
Z- impedance in Ohms
F- frequency in Hz
C- capacity of the skin in microfarads

## Slide 13: The Interference Effect

## Slide 14: Beat Frequency

## Slide 15: Constant Beat Frequency
Constant difference between the two circuits and this results in a constant beat frequency
If C1=4040Hz and C2=4000Hz, BF=40Hz
This is for 2 circuit devices
Allows frequency differences between 1-150Hz

## Slide 16: Variable Beat Frequency
Frequency between 2 circuits varies within pre-selected ranges, over a peroid of 5-10 secs
Variable beat frequency programs:
  0.1-1 bps
  1 to 10 bps
  1 to 120 bps
  90 to 120 bps
Quadripolar application

## Slide 17: Variable Beat Frequency

## Slide 18: Production of Interference Effect
Clover leaf Pattern

## Slide 19: Variations of Interference
Frequency Scale :
1 to 100Hz Constant
1 to 10 Hz Rhythmic
1-100 Hz Rhythmic
1-25 Hz Rhythmic
80- 100 Hz Rhythmic
Rhythmic indicates that the frequency swings continuously, changing the frequencies from the lower value to the higher value
Constant indicates that the IFC is as indicated by the scale

## Slide 20: Pre - Modulated IFC
Amplitude and frequency modulated beats are pre-mixed in the machine before it is delivered in the patient’s skin
Bipolar technique
No clinical evidence if it is better than the quadripolar technique

## Slide 21: Frequency Sweep
Used to overcome accommodation
Machine is set to automatically vary the effective stimulation frequency using pre-set or user set sweep ranges.

## Slide 22: Triangular Sweep Pattern
Up and down frequency in a time period of 6 secs
Only sweep pattern backed up by evidence

## Slide 23: Rectangular Sweep Pattern
Base and top frequencies are set then machine switches between two specific frequencies rather than gradually changing from one another

## Slide 24: Trapezoidal Sweep Pattern
Combination of the previous 2 sweep patterns

## Slide 25: Physiological Effects of IFT

## Slide 26: PHYSIOLOGICAL EFFECTS OF IFT
Analgesic effects :
The ‘pain-gate’ theory.
Descending pain suppression
Physiological block of nerve conduction
placebo

## Slide 27
Other effects:
Muscle stimulation
Increased blood circulation
Edema reduction
Placebo

## Slide 28: PAIN TRANSMISSION

## Slide 29: NOCICEPTORS
Sensory receptors located at free endings of Aδ and C fibers
Detect noxious stimuli
Carried to the CNS
Found in skin, viscera, muscles, joints, and meninges
They are stimulated by the inflammatory mediators released by the damaged tissue eg: bradykinins

## Slide 32: PRIMARY AFFRENT FIBERS
Nerves that carry input from the periphery to the spinal cord.
3 types: Aβ, Aδ and C fibers
FIBRE TYPE | STIMULI | ACTIVATION THRESHOLD | DIAMETER | MYELINATION | TRANSMISSION
Aβ | NON-NOXIOUS | LOW | LARGEST | HIGH | RAPID
Aδ | NOXIOUS, RAPID, SHARP, LOCALISED PAIN | HIGH AND LOW | SMALL | MODERATE | QUICK (but not as fast as Aβ)
C | NOXIOUS, SLOW, DULL, NON-LOCALISED PAIN | HIGH | SMALLEST | LOW | VERY SLOW

## Slide 34: ASCENDING THE SPINAL CORD
2 main pathways carry nociceptive signals up the spinal cord to the brain.
a) spinothalamic tracts
b) spinoreticular tracts
Pain processing in the brain
a) thalamus
b) primary and secondary somatosensory cortex
c) prefrontal cortex

## Slide 36: INHIBITING THE PAIN TRANSMISSION
GATE CONTROL THEORY
DESCENDING INHIBITORY PATHWAYS
PHYSIOLOGICAL BLOCK OF NERVE CONDUCTION

## Slide 37: 1) GATE CONTROL THEORY
Melzack and wall -1965
Inhibition at spinal cord level / pre synaptic inhibition
Eg: Rubbing over skin
Activates Aβ fibers
Activates inhibitory interneurons
Inhibits pain transmission by C fibers

## Slide 39
Transmission cell- ‘T’ in dorsal horn which prefers mechanoreceptor information rather than nociceptor information.
Nociceptive fibers i.e Aδ and C fibers relay in the more superficial lamina i.e say lamina 1 of the dorsal horn + areas of substantia gelatinosa.

## Slide 40
IMPULSES FIRE ON THE POLYSYNAPTIC INTERNEURONS
PROGRESS TO THE HIGHER CENTERS BY THE SPINOTHALAMIC TRACT
TO THE THALAMUS AND THEN THE PARIETAL LOBE

## Slide 41: POLYSYNAPTIC INTERNEURONS
They are cell bodies with dendrites present in the grey matter of the spinal cord. (present in the dorsal horn too)
Responsible for evoking motor response
Eg: when we suddenly step on a thorn
Sensory response- knowing that there was pain, location of the pain
Autonomic response- HR, RR

## Slide 42
Mechanoreceptors – rely on the polysynaptic interneurons in the deeper lamina of the dorsal horn and synapse with the spinocerebellar tract/ dorsal columns.
When there is increase in the mechanoreceptor activity, signals from the polysynaptic interneurons are not only transmitted to the spinothalamaic tract and dorsal column, but also fire back into the areas of Lamina 1 where the nociceptors usually fire.
Leading to a block in the polysynaptic interneurons in the nociceptor Lamina no pain conduction pre synaptic inhibition.

## Slide 43: 2) DESCENDING INHIBITORY PATHWAYS
Electrical stimulation of the periaqueductal grey matter (PAG) area can produce analgesia, demonstrated through electrophysiological and pharmacological studies that ‘descending influences’ on spinal nociceptive processing involves the PAG and the Rostral Ventromedial Medulla (RVM) (Fields, Milan -1960)

## Slide 44
(Dorsal Root Ganglion
Periaqueductal grey matter
Rostral ventromedial medulla
(DorsaHorn)
(Nucleus Raphe magnus)

## Slide 45
Incoming painful stimuli are transmitted
to the dorsal horn
to the Raphe nuclei, especially the nucleus raphe magnus, in the upper medulla
to the periaqueductal grey (PAG).
Descending impulses pass back Rostral ventromedial medulla (RVM)
to the dorsal horn via reticulospinal fibers.

## Slide 46
The periaqueductal grey matter (PAG) and the rostral ventromedial medulla (RVM) contain high levels of opioid receptors
Inhibition of the pain pathway occurs monoaminergically, releasing inhibitory neurotransmitters at the spinal level. (Goats 1990, Rennie 1988)
i.e through mono amine nerve transmitters – Nor adrenaline, dopamine, serotonin – also known as catecholamines.
Resulting analgesia may be long lasting , but pain may initially increase owing to the stimulation of nociceptive Aδ and C fibers (Goats,1990)
Post synaptic inhibition/ descending pain inhibition.
Notes: Monoaminergic means "working on monoamine neurotransmitters", which include serotonin, dopamine, norepinephrine, epinephrine, and histamine.

## Slide 47: 3) PHYSIOLOGICAL BLOCK OF NERVE CONDUCTION
Stimulation of peripheral nociceptive fibers at rates above their maximum conduction frequency may cause cessation of action potential propagation (De Domenico, 1982; Goats,1990; Low and Reed,2000 etal.), caused by increased stimulation threshold and synaptic fatigue (Goats,1990)

## Slide 48: OTHER EFFECTS
1) MUSCLE STIMULATION:
Stimulation of the motor nerves can be achieved with a wide range of frequencies. Clearly, stimulation at low frequency (e.g. 1Hz) will result in a series of twitches, while stimulation at 50Hz will result in a tetanic contraction. (Low And Reed; shafshak,El-Shehai and Soltan,1991)

## Slide 49
2) INCREASED CIRCULATION & EDEMA REDUCTION
Interferential current has been claimed to improve the circulation of blood and reduce swelling, which may wash away the chemicals that stimulate nociceptive nerve endings
Reduced swelling may concomitantly reduce tissue pressure. These phenomena are reported to occur because of mild muscle contraction or action on the autonomic nervous system, decreasing the tone of blood vessels
( Low and Reed; Shafshak,El-Sheshai and Soltan,1991)

## Slide 50
3) PLACEBO:
Placebo responses have been identified in the literature as a potential factor with IF stimulation (De Domenico,1982;Goats,1990; Low and Reed,2000; Rennie,1998; Taylor et al,1987) although they require verification.

## Slide 51: THERAPUTIC EFFECTS
Using high AMF (70-150 Hz) for acute problems and pain, and frequencies below 50Hz for chronic and sub-acute conditions and where muscle contraction is required.
A placebo effect, which occurs in all treatments, is likely, especially since interferential machines are technically impressive and produce a distinct, somewhat unusual but not unpleasant sensation.
Muscle contraction can also be achieved at higher current amplitude without any significantly uncomfortable skin sensation.
Stress incontinence in females (Laycock and Green, 1988), males (Laycock and Jerwood, 1993) using the bipolar technique increased strength in the pelvic floor muscles.

## Slide 52: The physiological effects on the tissues depend on the following factors:
The use of rhythmic or constant frequency swings
Intensity of current used
Accuracy of electrode placement with good calibration
Accurate localization of lesion
Patency of circulation and neurological function
Underlying pathophysiology in relation to desired effect

## Slide 53: 100 Hz Constant
Oscillations have marked amplitude and cause fine vibration of ions without producing heat.
Act on the sensory nerve endings, producing analgesis.
A 10-15 min stimulation can produce relief of pain lasting over an hour.
Inhibits the sympathetic system.
For RSD.

## Slide 54: 1 to 10 Hz Constant
More specific effect on motor nerves and causes muscle contraction.
Less sensory stimulus, greater depth of contraction and quite pleasant to feel than faradic- type currents
Can only stimulate normal innervated muscles

## Slide 55: 1 to 100 Hz Rhythmic
Alternate rhythmic excitation and relaxation of tissues producing more hyperaemia and increased cellular activity.
Caused by stimulating fine vibrations in the ions
Causes increase in blood flow, in tone of tissues and blood vessels
Aids in relief of oedema and in facilitating healing process (1-10 Hz)

## Slide 56: 90 to 100 Hz Rhythmic
Has analgesic and vasodilatory effects on tissues.
Particularly useful for neuralgic types of pain
Much less adaptation and habituation than with 100Hz constant.

## Slide 57: 1 to 10 Hz Rhythmic
Has a stimulating effect on motor nerves and tissues.
Vasodilatory effects
Has a vigorous pumping effect that aids in the absorption of exudates

## Slide 58: Impulse Current
A rectified medium frequency DC current surged at 50 Hz.
Frequency = 4000Hz
Pulse duration = 0.1ms
Produces a strong, sustained analgesic effect
Can be applied by bipolar technique

## Slide 59: Areas of Stimulation

## Slide 60: CLAIMED ANALGESIC MECHANISMS AND SUGGESTED AMF’S
THEORETICAL ANALGESIC MECHANISM | SUGGESTED AMF (AUTHOR)
‘PAIN GATE’/SENSORY FIBRE STIMULATION | 1-100Hz (WADSWORTH AND CHANMUGAM,1980) 80-100Hz ( DE DOMENICO,1982), 90-100 Hz (SAVAGE,1984) 100Hz (GOATS,1990)
INCREASED CIRCULATION/ SYMAPTHETIC FIBRE STIMULATION | 0-100Hz (WILLIE,1969); 0-5Hz (SAVAGE,1984) 100 Hz (GANNE,1976, NIKOLOVA,1987); 100Hz, 90-100Hz, 1-100Hz (WADSWORTH AND CHANMUGAM,1980) ; >80Hz (DE DOMINICO-1982)
DESCENDING PAIN SUPRESSION/ NOCICEPTIVE FIBRE STIMULATION | 10-25Hz (DE DOMINICO,1982) ; 130Hz (SAVAGE, 1984); 15Hz (GOATS-1990)
PHYSIOLOGICAL BLOCK OF NOCICEPTIVE FIBRES PLACEBO RESPONSE | C FIBERS>50Hz; Aδ FIBERS>40Hz (DE DOMENICO,1982); 40Hz LARGE DIAMETER/<40Hz SMALL DIAMETER (GOATS, 1990) NONE SPECIFICALLY IMPLICATED

## Slide 61: Advantage of four pole method
Lower strain on skin
Greater area of stimulation (when using vector method)
Allows focus of intensity in any localized area
(when using Static interference)
Suitable for treating deeper layers of tissue
No electrolytic skin effect and hyperemia as the current is bipolar.

## Slide 62: Disadvantage of four pole method
Difficult to position the electrode
Modulation depth is 100% at 45 degree only

## Slide 63: Advantage of two pole method
Small area can be treated by using bipolar method
Uses modulated current
Easy to apply

## Slide 64: Disadvantage of two pole method
Greater strain on skin
Amplitude is greatest along the line joining two electrode.

## Slide 65: Clinical Application

## Slide 66: Pain Relief
Stimulation of high frequencies (90-130 Hz) facilitates the gate mechanisms that masks the pain symptoms
Stimulation of lower frequencies (2-5Hz) activates the opioid mechanisms that provides a degree of relief.
Frequencies of 10-25 Hz stimulates the reticular formation while > 50 Hz blocks the C fiber transmission to relieve pain

## Slide 67: Pain Relief
Interferential Therapy provide substantive evidence of pain relief.(Hurley et al 2004, Johnson and Tabasam 2003, Walker et al 2006, McManus et al 2006, Jorge et al 2006.

## Slide 68: Pain Relief
Acute pain
  90 to 100 Hz rhythmic or 70-150 Hz
  Medium dosage
  10 mins.
Chronic pain
  100 Hz constant, 1-100 Hz rhythmic, or less then 50 Hz for neurogenic pain
  Medium dosage
  10 -15 mins.

## Slide 69: Muscle Stimulation
No significant evidence that has demonstrated a significant benefit of IFT over active exercise.
Note: Except for clinical circumstances where assisted contraction is beneficial.
Choice of parameters will depend on the desired effect.
Most effective motor nerve stimulation range= 10 and 20, 10 and 25 Hz
1-10 Hz rhythmic, high dosage, 5-10 mins. Up to 15 mins.

## Slide 70: Blood Flow
IFT demonstrated vascular changes at 10-20 Hz although the experiment was unable to clearly identify the mechanism for change (Noble et al,2000)
The most likely mechanism is via muscle stimulation which brings about a local metabolic and vascular change in the tissues.

## Slide 71: Edema
Evidence is very limited
Mechanism: Local muscle contraction combined with local vascular changes will result an effective reabsorption of tissue fluid.
1-10 Hz Rhythmic is effective

## Slide 72: Indications and Contraindications

## Slide 73: Indications
Pain
Muscle spasm
Edema
  Rhythmic 1 -100 Hz or 1-10 Hz
Hematoma
  100 Hz constant, then with US
Chronic ligamentous lesions
Trigger spots on myofascial syndromes
  Constant 100 Hz and rhythmic 1-100 Hz
Stress incontinence
  1-10 Hz rhythmic or
  1-100 Hz rhythmic for 15 minutes
Delayed union
  100 Hz constant, moderately strong dose, 15 mins.
Epicondylitis
Retarded callus formation
Raynaud’s disease

## Slide 74: Contraindications
Arterial disease
DVT
Infective conditions
Pregnant uterus
Hemorrhage
Malignant tumors
Artificial pacemakers
Sensory loss
During menstruation
Febrile conditions
Large open wound
Unreliable patients
Dermatological conditions

## Slide 75: Again, how does IFT produces interference current?
Interferential Therapy utilizes two medium frequency currents, passed through the tissues simultaneously, where they are set to cross paths and literally interfere with each other. The interference gives rise to a beat frequency similar to low frequency stimulation.

## Slide 76: References:
Clinical Electrotherapy by Roger M. Nelson & Dean P. Currier
Clayton’s Electrotherapy by Sheila Kitchen & Sarah Bazin
Principles and Practice of Electrotherapy by Joseph Kahn
Electrophysical Agents in Physiotherapy Therapeutic and Diagnostic Use by Hilary Wadsworth & A.P.P. Chanmugam
Physical Agents 2 Archives by Leonardo M. Mariano, Jr., PTRP
www.electrotherapy.org
Interferential Current Therapy in Clinical Practice. 1993. by Samuel Davis, PT

## Slide 77: Thank You!

## Slide 79
Capacitive Coupling
  The ratio charge to potential on an electrically charged isolated conductor

## Slide 80: Electrokinesy
50 with a 4000 Hz current
Useful for patients with pain and muscle spasm by “deblocking” the spasm of strong muscle contractions for 2-3 minutes.